## Slide 1: RSPT 2335
INTRODUCTION
&
Part 1
Pharyngeal, Laryngeal & Esophageal Airways
MODULE A
AIRWAY MANAGEMENT

## Slide 2: Parts of Module A AIRWAY MANAGEMENT
Part 1 – Pharyngeal, Laryngeal & Esophageal Airways
Part 2 – Tracheal Airways
Part 3 – Airway Clearance
Part 4 - Advanced Airways
Part 5 - Airway Complications & Emergencies

## Slide 3: ASSIGNMENTS MODULE A
Reading:
  Egan’s Fundamentals of RC:
    Chapter 33 – 746-747, 754-756, 760-764, 767-779

## Slide 4: ASSIGNMENTS
Laboratory Work:
  Butler
    22.2.3 – Intubation with an ETC airway in place
    22.3 – Securing an ET tube
    22.2.5 – Nasotracheal intubation
    23.2.3 – Tracheostomy tube decannulation
    24.2 – Resecuring and repositioning of an endotracheal tube and oral hygiene
    24.3 – Extubation
    24.4 – Airway emergencies

## Slide 5: RESOURCES
AARC-Clinical Practice Guidelines:
  “These AARC’s guidelines enhance respiratory practice and provide a framework for RT protocols. “
    Endotracheal Suctioning of Mechanically Ventilated Patients with Artificial Airways (revised 2010)
    Nasotracheal Suctioning
    Removal of the Endotracheal Tube (revised 2007)
    Bronchoscopy Assisting

## Slide 6: RESOURCES
Other Guidelines:
  ASA - Practice Guidelines for Management of the Difficult Airway

## Slide 7: OBJECTIVES
At the end of this module, the student should be able to…
  identify the different laryngeal & esophageal airways , their components and accessories.
  list the indications, contraindications, hazards & complications of these airways.
  list the advantages and disadvantages of the these airways.

## Slide 8: OBJECTIVES
At the end of this module, the student should be able to…
  demonstrate the ability to determine the proper size airway for a patient.
  demonstrate the ability to insert, check proper placement and secure these airways.
  demonstrate the ability to perform airway maintenance.

## Slide 9: OBJECTIVES
At the end of this module, the student should be able to…
  explain the proper procedure for removal of the these airways.
  given a problem scenario, describe the proper procedures for handling the situation.

## Slide 10: Major Topics
Laryngeal Airways
Esophageal Airways

## Slide 11
Airway Placement:
Oral Pharynx
Nasal Pharynx
Larynx
Isolation (esophageal)
Orotracheal
Nasotracheal
Tracheal

## Slide 12: Laryngeal Airway Devices (Supralaryngeal)
Laryngeal Mask Airway
(LMA)

## Slide 14
B. Anatomy

## Slide 15
Airway Placement:
Oral Pharynx
Nasal Pharynx
Larynx
Isolation (esophageal)
Orotracheal
Nasotracheal
Tracheal

## Slide 16: Laryngeal Mask Airway (LMA)
Most common uses in U.S. since 1991:
  Popular in Operating Rooms especially for difficult intubations or short surgeries (ambulatory anesthesia)
  Use in Emergency Department especially for difficult or failed intubations
  Option for difficult intubation and airway management
  Some success with surfactant administration in neonates

## Slide 18
Egan pg. 778 Fig. 33-38 Laryngeal mask airway

## Slide 19
Insertion – (LMA)
  Be sure the cuff is deflated and then lubricate the posterior surface of the airway only.
  Do not use anesthetic sprays in the airway.
  The unconscious patient is placed in the sniffing position
  A conscious patient should have some form of sedation (similar to endotracheal intubation)

## Slide 20
Insertion – (LMA)
  The jaw is held open and the mask and cuff are advanced along the hard palate
    Some may be inserted without putting finders into the mouth
    Others require using the index finger to move the mask into position at the back of the tongue in the esophageal sphincter.
  The tube is advanced until resistance is felt as the mask settles over the esophagus and larynx.

## Slide 21
Insertion – (LMA)
  The cuff is inflated around the laryngeal opening
    There may be a small swelling noted at the level of the cricoid cartilage in the neck.
    Inflation pressure may reach 60 cmH2O
    Fill until the pilot balloon is firm but not hard.
    Inflation volume varies with LMA size and patient anatomy (4 – 50 mL)

## Slide 22: Troubleshooting– (LMA)
What if I insert the LMA, inflate the cuff and there is still a leak?
  Verify the proper LMA size
  Verify the correct amount of air was used to inflate the cuff (to much and too little can cause leaks
  Deflate the cuff, reposition the LMA and re-inflate
  Flex the patient’s neck 10 – 20 degrees
  Verify that the ventilating pressures do not exceed to pressure limit of the LMA (usually 20 cmH2O)
  Change to pressure control ventilation (handles leaks better)
  Ensure the patient is properly sedated/anesthetized or unconscious

## Slide 23: Laryngeal Mask Airway (LMA)
Advantages
  Placed blindly - Quick with no additional equipment needed
  Low pressure seal around glottis may cause less trauma than endotracheal intubation.
  Spontaneous breathing is possible.
  An endotracheal tube may be inserted directly into the trachea through some LMAs.

## Slide 26
Egan Fig. 33-38
Intubating laryngeal mask airway.

## Slide 27: Laryngeal Mask Airway (LMA)
Contraindications
  Conscious or semi-conscious patients (non-sedated)
  Patients with high risk of aspiration
Removal
  The airway can be removed when the patient is alert enough to open their mouth on command.

## Slide 28: Laryngeal Mask Airway (LMA)
Disadvantages
  It does not reliably prevent aspiration.
  May stimulate gag reflex or laryngospasm.
  High pressure assisted ventilation may cause gastric insufflation.
  Usually used with ventilating pressures of 20 cm H2O or less. (Pro-seal up to 30 cm H2O)

## Slide 30: Reusable LMA
May be reused up to 40 times
Better have a good tracking system needed!
Processing:
  Clean with appropriate solution
    Endozyme, 1:10 baking soda & water, mild detergent
  Rinse & inspect
  Dry & deflate cuff
  Package
  Sterilize by Steam Autoclave only
Check performance before next use

## Slide 31: Esophageal (Isolation) Airways

## Slide 32: Esophageal Airway (Isolation) Devices
Esophageal Tracheal Combitube (ETC) (Double-lumen)
King Airway

## Slide 33
Available in two adult sizes based on height
Combitube SA (small adult)
4 – 5.5 feet tall
And
Combitube
5 feet and over

## Slide 34
Comes packaged with two syringes
20 mL & 140 mL

## Slide 36
Egan pg. 779
Fig. 33-40 Insertion of the Combitube.
Esophageal placement
Tracheal placement

## Slide 37: Esophageal Tracheal Combitube (ETC)
Uses in U.S. since 1988:
  for adult victims
  unresponsive without gag reflex
  popular on EMS transports when intubation is not possible or permitted
  patients may enter ED with device
  may be used for difficult airway management

## Slide 38
Insertion
  The jaw is held open and the tube is advanced along the hard palate until teeth are between reference marks
  It may be placed into the esophagus or the trachea.
  Do not force – if resistance is met; redirect or withdraw and reinsert.

## Slide 39
Insertion
  Cuffs are inflated with syringes
    Proximal Blue #1 with 85 - 100 mL air (140 mL syringe)
    Distal White #2 with 10 - 15 mL air (20 mL syringe)
  Attempt ventilation through longer tube first
    If negative - then try shorter tube
    If negative – then deflate cuffs and adjust depth (pull back 1 – 2 cm)

## Slide 40
Esophageal placement
(most likely)
  Both cuffs remain inflated
  The bag is attached to long blue port #1
  gas will move through the side hole on the lower tube and into the lungs
  Second tube can be used for gastric suction
  If long-term ventilation is needed:
    May intubate before removing ETC

## Slide 41
Tracheal intubation:
  only the lower cuff needs to remain inflated
  the bag is attached to shorter white port #2.
  Deflate larger balloon if desired
  If long-term ventilation is needed:
    May remove to intubate
    May use tube exchanger or bougie for intubation

## Slide 42
Tube Changer
(exchanger)

## Slide 43: ETC
Removal of ETC
  remove if patient is capable of sustaining spontaneous respirations on their own
  If long-term ventilation is needed
Contraindications –
  Not for use with esophageal trauma or disease, corrosive ingestion, pharyngeal trauma.
  Positive gag reflex

## Slide 44: ETC
Advantages
  Blind placement (95% in esophagus)
  High ventilation pressures possible
  Ability to suction stomach (with esophageal placement)
  Spontaneous breathing is possible.
  There is no concern about head position or mask seal.

## Slide 45: ETC
Advantages
  Pharyngeal balloon is self-adjusting and self positioning.
  If in the esophagus, it does not stimulate the larynx so spasm of the vocal cords is not a problem.
  Does not require laryngoscope to insert.
  Can be placed in esophagus or trachea and still be useful.

## Slide 46: ETC
Disadvantages
  May cause esophageal perforation.
  Could cause same complications as an endotracheal tube.
  Must use caution to keep cuffs in place and inflated properly.
  Must be sure to bag through the appropriate port.

## Slide 47: Replacing ETC in Esophagus
1. Prepare equipment
  resuscitation bag & mask
  Intubation
  Suctioning
Prepare the patient
  Inform
  Position
Suction ETC & upper airway
Deflate the upper cuff
Insert the ET
Ventilate the patient and verify ET placement
Inflate ET cuff
Hold the ET, deflate ETC lower cuff and remove
Secure ET and check cuff pressure

## Slide 48: Replacing ETC in Trachea
1. Prepare equipment
  resuscitation bag & mask
  Intubation
  Tube exchanger
  Suctioning
Prepare the patient
  Inform
  Position
Suction ETC & oral airway
Deflate the cuff(s)
Perform the “Cuff Leak Test”
Insert a “Tube Exchanger”
Remove the ETC
Insert the ET tube
Remove the tube exchanger
Ventilate, verify tube placement & secure

## Slide 49: King Airway

## Slide 50: King Airways
LTS-D
LTS
LT-D
D=disposible

## Slide 51
KING LT-D
Placement into the esophagus
Two cuffs:
  One cuff smaller lower cuff prevents gastric distension
  Larger upper cuff seals upper airway
Gastric tube cannot be passed for decompression
Cannot intubate using tube exchanger

## Slide 52: Ventilation Ports

## Slide 54: LT-D Insertion Videos
http://www.youtube.com/watch?v=eJix_gZW5OA&feature=related
http://www.youtube.com/watch?v=ca710sG4-ck

## Slide 55
KING LTS-D
Placement into the esophagus
Two cuffs:
  One cuff smaller lower cuff prevents gastric distension
  Larger upper cuff seals upper airway
Gastric tube can be passed for decompression
Can intubate using tube exchanger
NOTE: King LTS is Reusable up to 50 times

## Slide 56: Sizes
Yellow
  4 – 5 feet tall
  45 - 60 mL air in cuff
Red
  5 – 6 feet tall
  60 – 80 mL air in cuff
Purple
  Over 6 feet tall
  70 – 90 mL air in cuff

## Slide 57
King LTS-D in place

## Slide 59: Advantages
Easy insertion
Esophageal placement only
Single inflation line for both cuffs
Single ventilation connection
Good ventilatory seal for pressures > 30cmH2O
Airway exchange possible
Easy access to stomach (LTS-D)

## Slide 61
King LTS-D
Gastric tube in place

## Slide 63: NG Tube Insertion Procedure

## Slide 64: NG Tube

## Slide 65: Measuring Length of an NG Tube

## Slide 66: NG Tube Placement

## Slide 67: Securing an NG

## Slide 68: Checking NG Tube Placement

## Slide 69: NG Tube Insertion (MITS)
Measure
Insert
Test
Secure

## Slide 70: Practice inserting an NG tube
Measure:
  Ear lobe to tip of nose to xiphoid process
  Place a piece of tape on NG tube to mark depth
Position patient
  Head neutral or flexed slightly forward for entrance into esophagus
Lubricate & insert (ask patient to swallow)
Verify placement
  Use large syringe to inject air
  listen for bubbling over stomach
Tape in place
  DO NOT TAPE TO ET TUBE

## Slide 72
SLIPA - Streamlined Liner of the Pharynx Airway

## Slide 73: SLIPA
Single-use supralaryngeal airway
Used for positive pressure ventilation (up to 30 cmH2O)
For use in anesthesia & emergency airway management
Cuffless
Seals at the base of the tongue
Hollow device can capture 50 mL of regurgitated fluid

## Slide 78: Pharyngotracheal Lumen Airway (PTL) (Double-lumen)
Rarely used – replaced by combitube.
See display board for sample