## Slide 1: RSPT 2335
Module A
AIRWAY MANAGEMENT
Part 2a
Tracheal Airways

## Slide 2: Parts of Module A AIRWAY MANAGEMENT
Part 1 – Pharyngeal, Laryngeal & Esophageal Airways
Part 2 – Tracheal Airways
Part 3 – Airway Clearance
Part 4 - Advanced Airways
Part 5 - Airway Complications & Emergencies

## Slide 3: OBJECTIVES
At the end of this module, the student should be able to do the following regarding tracheal airways…
  identify airways, components and accessories
  list indications, contraindications, hazards & complications, advantages and disadvantages
  prepare, insert, place and secure
  airway maintenance including cleaning, securing and cuff pressures.
  airway removal
  use speaking devices & buttons.
  educate a patient going home with an airway.

## Slide 4: RESOURCES
AARC-Clinical Practice Guidelines:
  “These AARC’s guidelines enhance respiratory practice and provide a framework for RT protocols. “
    Endotracheal Suctioning of Mechanically Ventilated Patients with Artificial Airways (revised 2010)
    Nasotracheal Suctioning
    Management of Airway Emergencies
    Removal of the Endotracheal Tube (revised 2007)
    Bronchoscopy Assisting

## Slide 5: RESOURCES
Other Guidelines:
  ASA - Practice Guidelines for Management of the Difficult Airway

## Slide 6: Major Topics
Oral Intubation Verification & Stabilization
Nasal Intubation
Ventilator Associated Pneumonia
Alternative Airways & Accessories
Exchanges & Extubation
Tracheostomy Airway Insertion & Changes
Humidity & Oxygenation
Laryngectomy
Communication Devices
Decannulation
Home care

## Slide 7: Oral Intubation Verification & Stabilization

## Slide 8: Oral Intubation
Uncomplicated Endotracheal Intubation
  Review & Practice on your own
Confirming Placement
Securing

## Slide 9
Lab Chapter 22.1.2
Page 351
Identification of the Components of an endotracheal tube

## Slide 10: Endotracheal Airways
Oral endotracheal tubes
Nasal endotracheal tubes

## Slide 11: Confirming Placement in the Trachea and Depth
During intubation
Depth markings
Physical Assessment
Bedside Tools
Radiography

## Slide 12
During intubation:
  Observe cuff passing through the cords 2 - 3 cm or 1 – 2 inches and then stop.
Confirming Placement

## Slide 13: Confirming Placement
Physical Assessment
  Palpate for symmetrical chest movement
  Visualize
    symmetrical chest movement
    condensate inside the ET tube corresponding to exhalation
  Auscultate
    bilateral breath sounds (upper & middle)
    epigastrium to verify there are no ventilation sounds
  Observe clinical improvement in color, heart rate, pulse oximetry

## Slide 14: Confirming Placement
Use Tools
  Pass a suction catheter
    Should meet resistance
    May stimulate cough
  Esophageal detector devices (> 1 yr. olds)
    Bulb - Squeeze bulb and if re-inflation occurs then ETT is in trachea
    Syringe - Draw back on syringe and if re-inflation occurs then ETT is in trachea

## Slide 16: Confirming Placement
Tools for confirming placement in trachea
  CO2 detectors - requires metabolism at the tissues, blood flow to the lungs and ventilation of the lungs to display CO2
    Capnograph - displays CO2 in mm Hg and gives waveform.
    Colorimetric - shows color change (purple/blue to yellow) in presence of CO2
      small & inexpensive with two sizes available
      readily available & easy to use
      fast acting (after 6 breaths)
      disposable (after approx. 2 hours)
      sensitive to H2O

## Slide 17: Confirming Placement
Capnogram tracing showing changes in expired percent CO2
A disposable colorimetric CO2 detector

## Slide 20: Confirming Placement
Tools for confirming placement in trachea
  Lighted wand - Insert down ETT after intubation an if it illuminates neck , the tube has been placed in trachea.
  Bronchoscopic visualization of carina or tracheal rings through the tube.

## Slide 21: Confirming Placement
Radiography for confirming placement
  Chest radiograph - most reliable technique but takes the longest to obtain
    Radiopaque line on ETT can be visualized easily
    Lateral for tracheal placement

## Slide 22: Confirming Depth
Radiography for confirming depth
  Chest radiograph - most reliable technique but takes the longest to obtain
    Radiopaque line on ETT can be visualized easily
    AP or PA for depth

## Slide 23: Critical Thinking Question 22-4
Describe in specific radiologic terms the proper location of an endotracheal tube.
  Answer: Tube tip should be…
  1. 2 -3 cm or 1 inch below the cords
  2. 2 - 7 cm above the carina at T2 - T4 (2 - 3 in.)
  3. At the level of the aortic knob/notch
  4. Mid-trachea

## Slide 24
ET Level
Carina Level

## Slide 25
Depth:
ORAL ETT
Tip to lip in cm
NASAL ETT
Tip to nare in cm
MALE
21 – 23
22 – 24
(Pilbeam)
23 - 25
FEMALE
19 – 21
20 – 22
(Pilbeam)
21 - 23
Marking of depth on tube
Confirming DEPTH not placement

## Slide 26: Securing & Retaping

## Slide 27
Do not let go of the ETT !!!!!!!!
  Carefully remove laryngoscope
  Carefully remove stylet
  Inflate cuff with enough air (approx. 5 mL) to get gentle pressure in pilot balloon
  Ventilate and oxygenate the patient
  Secure per hospital protocol
Securing the Airway

## Slide 28: Securing the Airway
Keep head in neutral position (especially infants)
  Head flexing moves tube down as much as 3 cm
  Head extension raises tube out as much as 5 cm

## Slide 29: Securing the Airway
Secure tube with:
  Non-porous, water-proof tape
  Elastoplast
  Umbilical tape
  Pre-fabricated harness devices
    Anchor Fast
    Dale ET tube holder
    SecureEast ET Holder
Do not tape gastric tube to tracheal airway!

## Slide 30
Do not use oral airway as a bite block
Securing the Airway

## Slide 31
Securing the Airway

## Slide 33: Anchor Fast
http://www.hollister.com/us/tube/learning/popup_video.asp?video=AnchorFast
Securing the Airway

## Slide 34
http://www.neotechproducts.com/products/neobar/
(Page down to bottom)
Securing the Airway

## Slide 35: NEO-fit™ Neonatal Endotracheal Tube Grip
Securing the Airway

## Slide 36: Retaping
Prepare equipment for retaping:
  new tape
  shaver
  wet and dry wash cloth
  suction kit and yankauer catheter
  tincture of benzoine
Do not let go of the ETT !!!!!!!!

## Slide 37: Retaping
Remove old tape and do not remove hand from ETT
Perform oral care
Wash face
Males may be shaved but use care not to cut pilot balloon
Apply tincture of benzoin on gauze then dab on face
Re-tape tube and verify correct depth

## Slide 38: Lab Chapter 22.3
Do Exercise 22.3 – Securing an Endotracheal Tube
  NOTE: Do not use OPA as a bite block

## Slide 39: Ventilator Associated Pneumonia (VAP)

## Slide 40: Nosocomial Infections
Statistics:
  Nearly 2 million patients in U.S. hospitals get a healthcare-associated infection (HAI) each year. (5% – 10% of all admissions)
    40% of these infections are respiratory infections
    86% of these respiratory infections are linked to mechanical ventilation/tracheal airways and are called Ventilator Associated Pneumonia (VAP)
    VAP is second most common nosocomial infection in US

## Slide 41: Nosocomial Infections
“Aspiration of oral and/or gastric secretions is the primary route of bacteria entry into the lungs and is believe to be the primary factor in the
development of VAP”

## Slide 42: Ventilator Associated Pneumonia
Statistics:
  According to the AJCC, Ventilator Associated Pneumonia occurs in up to 65% of ventilated critical care patients.
  VAP is associated with increases in patient ICU time by up to 22 days
  Each incident of VAP is estimated to increase cost by as much as $40,000

## Slide 43: Ventilator Associated Pneumonia
Statistics:
  About 90,000+ will die annually as a result of VAP
  VAP may account for 60% of all deaths due to Healthcare-Associated Infections (HAI)
  Mortality that is directly attributable to VAP is estimated to be as high as 27.1%

## Slide 44: What can we do about VAP???? 1. Read: Pilbeam Chapter 17: pages 294-305 2. Watch AARC Professor’s Rounds DVD: Minimizing VAP in 2011 – How Respiratory Therapists Can Contribute 3. Take post DVD quiz

## Slide 45: Strategies for VAP Prevention
1. GENERAL STRATEGIES
  Manage health care associated infection (HAI). as sentinel events
  Educate healthcare providers
  Conduct surveillance for VAP
    Monitor for symptoms - sputum, breath sounds, chest radiograph, fever, WBC (>10% bands neutrophils)
  Focus on prevention rather than treatment

## Slide 46: Strategies for VAP Prevention
2. Respiratory Therapy Strategies
  Hand hygiene
  Avoid intubation - use NPPV when possible
  Orotracheal intubation preferred over nasotracheal
  30 – 45 degree elevation of patient’s head
  Avoid gastric over-distension

## Slide 47: Strategies for VAP Prevention
  Speed up extubation - decrease ventilator days with daily weaning assessment and weaning protocols
    Weaning pathway (TDP)
    Sedation “holiday”
    Avoid unplanned extubation and reintubation
  Maintain cuff pressure of at least 20 mm Hg (27 cm H2O) or minimum occlusive volume/pressure
  Use newer style cuffed ET tubes with subglottic suctioning

## Slide 49: SealGuard Evac Endotracheal Tube
http://www.covidien.com/rms/products/endotracheal-airways/mallinckrodt-taperguard-evac-oral-endotracheal-tube#resources (10:22)

## Slide 50
Fluid remains above the Kimberly-Clark Microcuff

## Slide 51: Silver Coated Endotracheal Tubes
Research found that in the population with the silver-coated endotracheal tubes:
  VAP in all its forms was reduced by nearly 40 percent
  highly resistant infections were less than half as likely to occur in those with the silver-coated tubes.
Used to reduce “Time to VAP” occurrence
Prevents bacterial colonization and biofilm formation on tube

## Slide 52
Endotracheal tube with suction port above the cuff.
Facilitates the removal of pharyngeal secretions that accumulate above the cuff.
May help decrease the incidence of nosocomial pneumonia. (VAP)
Continuous Aspiration of Subglottic Secretion (CASS)

## Slide 53
Continuous Aspiration of Subglottic Secretion (CASS)
Processes:
Continuous suction -20 to -60 mm Hg
Or
Intermittent suction -100 to -150 mm Hg
May inject manual air bolus into suction lumen to assure patency as needed.

## Slide 54: Critical Thinking Question
Your male patient is intubated with a 7.0 mm orotracheal tube. He is in ICU on a ventilator. The low-exhaled-volume alarm is sounding, and he is phonating. His respiratory rate is 32/min., the heart rate is 122/min., and the pulse oximeter is 89%. You measure the cuff pressure to be 30 cmH2O, and the pilot tube and valve are intact.
What would be your recommendations to remedy this situation?

## Slide 55: Cuff pressures (Pilbeam)
20 – 25 mm Hg or Torr
27 - 34 cm H2O

## Slide 56: Strategies for VAP Prevention
More Respiratory Therapy Strategies
  Perform regular oral care with an antiseptic solution

## Slide 57: Importance of Oral Care
Studies have shown some of the major risk factors for VAP include:
  Bacterial colonization of the oral pharynx
  Aspiration of subglottic secretions
  Colonization of dental plaque

## Slide 58: Oral Care Procedure
Prepare equipment for oral care (no kits)
  PPE (gloves, fluid shield)
  lemon glycerin swabs or sponge swabs
  or tooth brush and tooth paste
  ½ strength mouthwash
  basin
  suction and yankauer catheter

## Slide 59
Many products now available include:
Suction tooth brush
Suction swab
Covered yankauer
Peroxide solutions
Oral rinse
Antiplaque solution
Mouthwash

## Slide 60: Strategies for VAP Prevention
More Respiratory Therapy Strategies
MINIMIZE VENTILATOR EQUIPMENT CONTAMINATION
  Minimal opening of the ventilator circuit
  Sterile technique with suctioning & closed suction systems
  Remove condensate from ventilator circuits but keep circuit closed during removal
  Filter gases (inspiratory & expiratory)

## Slide 61: http://www.youtube.com/covidienplc#p/a/u/2/ZmVmm2viFOs
Why should we use filters?
Why shouldn’t we break the circuit?

## Slide 62: Strategies for VAP Prevention
More Respiratory Therapy Strategies
MINIMIZE VENTILATOR EQUIPMENT CONTAMINATION
  Use sterile water to rinse reusable equipment
  HME use if not contraindicated and change HMEs Q 48 hours unless visibly soiled or malfunctioning
  Change circuits only when soiled or malfunctioning
  Disinfect and store equipment properly

## Slide 63: Strategies for VAP Prevention
3. Other Strategies
REDUCE DIGESTIVE TRACT COLONIZATION
  NG tube placement
  Feed Patient: Parenteral nutrition or Duodenum feedings (J tube or Dobhoff)

## Slide 64: Strategies for VAP Prevention
3. Other Strategies
  Deep vein thrombosis prophylaxis (DVT)
  Avoid acid-suppressive therapy when not indicated for stress ulcers or gastritis
  If indicated – use stress bleeding prophylaxis (gastric H2 blockers or sucralfate)
  Tight glycemic control

## Slide 65: Lab Chapter 24
Oral Care Videos:
http://www.sageproducts.com/products/oral-hygiene/video.cfm?name=RXThumbPort
http://www.kchealthcare.com/products/respiratory-health/kimvent-oral-care-solutions.aspx
http://www.intersurgical.com/products/critical-care/oral-care#videos
Do Exercise 24.2
  Re-securing and Repositioning of an Endotracheal Tube
  Practice Oral Care procedure

## Slide 66: Alternative Airways and Accessories

## Slide 67: Hi-Lo™ Endotracheal Tube with Lanz™ Pressure Regulating Valve
Lanz™ valve automatically maintains intra-cuff pressure to approximately 30 cm H2O.
Lanz™ valve reduces the need for manual cuff pressure monitoring.

## Slide 68
Anode or (Deane) tube has spiral steel reinforcing wire which prevents kinking when the tube must be bent out of the way of a surgical field
Spiral Steel Reinforcing Wire

## Slide 69
Nasal RAE™ Endotracheal Tube
Preformed curve removes circuit from surgical field.
Unique design helps protect against kinks and disconnects.
Indications For Usage
Oral Surgery
Maxillofacial surgery

## Slide 70: Emergency Medicine Tube (MET)

## Slide 71
Double Lumen Endobronchial Tube

## Slide 72
Infant & Pediatric Endotracheal Tubes
Cuffless endotracheal tube
May be uncuffed up to
size 5.5 – 6 mm ID
or
4 – 6 yrs. old

## Slide 74: Pediatric Cuffed ET Tubes

## Slide 75
Infant & Pediatric Endotracheal Tubes
Cole – tapered airway
Not in use any more

## Slide 76: Pediatric ET Size Calculations
8 & older:
Size of ET tube (ID) = age in yrs - (age/4) (8 yr: 8-2=6)
OR
Size of ET tube (ID) = 16 + age in yrs (8 yr: 24/4=6)
4
2 years and older:
Age 2 years uses 5.0 mm and for every two years thereafter up to 14 years add 0.5 mm
(8 yr = 5 + 1.5 = 6.5)

## Slide 77: Pediatric ET Depth Calculations
1. Pediatric ET Depth = 12 + (age/2)
OR
2. Infant ET tube depth use “Rule of Seven”
1 kg = depth of 7cm @ lip
2 kg = depth of 8cm @ lip
3 kg = depth of 9cm @ lip
4 kg = depth of 10cm @ lip

## Slide 78
Use the Chart

## Slide 79: Broselow™ Pediatric Resuscitation System

## Slide 80: Broselow™ Pediatric Resuscitation System

## Slide 82: Infant Practice
Selecting equipment
Intubation
Positioning
Securing

## Slide 83: Exchanges & Extubation

## Slide 84: ET Tube Exchanges

## Slide 85: Exchanging the ET Tube
Reasons:
  Cuff torn
  Pilot line cut
  Pilot valve broken
  Larger or different tube needed
  Airway becomes obstructed

## Slide 87
Use of a Tube Changer
Most important job - Keep changer at correct marking at teeth

## Slide 88: ET Tube Extubation

## Slide 89: Considerations Before Extubation
Assess readiness
    Has original need for airway been resolved???
Get permission
    Physician order
    Protocol

## Slide 90: Why Extubation?
Endotracheal tube is no longer needed for…
Ventilation – can breath on their own
Oxygenation – can oxygenate without ET
Airway control – has no obstruction or swelling
Airway protection – has adequate LOC, swallow & gag
Airway clearance – can cough & clear secretions with acceptable production

## Slide 91: Why Extubation?
Other Reasons:
Terminal Weaning - Patient in whom further medical care is deemed futile
Obstruction - Acute artificial airway obstruction

## Slide 92: Q#57. A 2 yr-old child with croup has been intubated for 4 days with a 4 mm ID uncuffed endotracheal tube. Heated aerosol at an FiO2 of .21 has been delivered to the intubated patient. The physician asks the therapist to evaluate the patient for possible extubation. Which of the following would most likely indicate that the patient is ready for extubation?
The patient is making normal quiet ventilator efforts
A negative sputum culture and sensitivity has been reported
The patient’s ABGs are within normal range
Breath sounds are heard around the tube on auscultation
15

## Slide 94: How would you assess before extubation?
Ventilation – Spontaneous breathing trial (SBT)
Oxygenation – SpO2 with FiO2 and PEEP at low levels
Airway control – Cuff Leak Test
Airway protection – Check LOC, swallow and gag
Airway clearance – check cough and sputum production

## Slide 95
Perform airway cuff leak test
Clear upper airway secretions
Deflate cuff
Occlude tube
Peritubular leak should occur on spontaneous respirations (or with bag ventilation)

## Slide 96: What should be done if the patient fails the “Cuff Leak Test”???
Pre-treat with steroids
Pre-treat with racemic epinephrine (alpha agent)
Use cool aerosol set-up rather than nasal cannula after extubation

## Slide 97: Preparation for Extubation:
Gather and prepare equipment:
  personal protection equipment
  suction equipment: open or closed and yankauer
  oxygen set up
  resuscitation bag & mask
  Monitoring equipment (ECG, pulse oximeter…)
  10 mL syringe
  scissors
  treatment nebulizer and Alpha agent (i.e., epi)
  re-intubation supplies

## Slide 98: Preparation for Extubation:
Prepare yourself:
  Wash hands
  Put on PPE (gloves and fluid shield)
Prepare the patient:
  Discontinue tube feeding 4 – 6 hours prior
  Explain procedure to patient
  Place patient in semi or high fowlers
  Attach pulse oximeter
  Hyperoxygenation pre & post suction
  Suction oral pharynx and above the cuff
  Suction the ETT

## Slide 99: Preparation for Extubation:
Prepare the tube:
  Deflate the cuff while squeezing the bag or having the patient cough (moves secretions from above cuff to mouth)
QUESTION: Why is it inappropriate to cut the pilot balloon prior to extubation?
  The vocal cords would be used to cause cuff deflation
  Vocal cord damage could occur
  Tube is useless in case emergency reintubation is required.

## Slide 100: Preparation for Extubation:
Perform airway cuff leak test *
  Clear upper airway secretions
  Deflate cuff and occlude tube
  Peritubular leak should occur on spontaneous respirations or mechanical breath
Cut the tape

## Slide 101: The Extubation Procedure:
Methods for removing the tube:
  Have the patient take a deep breath then either
    pull tube at peak inspiration (cords open)
    cough and pull tube at peak inspiration (cords open)
    squeeze the resuscitation bag and pull tube at peak inspiration (cords open)
  Not Recommended: Suctioning as the tube is removed

## Slide 102: Post - Extubation Procedure:
Have the patient cough to clear any retained secretions.
Apply oxygen device (usually nasal O2)
Assess patient
  Breath sounds and airway patency
  Vitals & LOC
  Oxygenation (SpO2)
  Ventilation (ABG)
  Work of breathing
  Ability to clear secretions
Keep patient NPO x 24 hours (ice chips and small water sips only) to prevent post extubation aspiration

## Slide 103: Extubation Complications Immediate
Observe for immediate complications associated with:
  laryngospasm
  glotic edema
  supraglottic obstruction
  pulmonary aspiration
  impaired gas exchange
  pulmonary edema

## Slide 104: What should be done if the patient develops laryngospasm?
Transient:
  Bag & mask ventilation with Oxygen
Persistent:
  Neuromuscular blockade
  Reintubation

## Slide 105: Extubation Complications
IMMEDIATE POST-EXTUBATION COMPLICATIONS
MANAGEMENT
Severe (marked, extreme…) inspiratory stridor or respiratory distress
REINTUBATE
Moderate distress/stridor
Oxygenate, cool mist aerosol and racemic epinephrine, steroids to reduce swelling and possible heli-ox
Mild distress/stridor or sore throat and hoarseness, cough
Provide aerosol therapy, oxygen and/or racemic epinephrine as needed

## Slide 106: REINTUBATION STATS
Increases risk of getting nosocomial pneumonia eightfold
Is associated with a 6 – twelvefold increase in mortality
Nearly 80% of patients who self-extubate do not require reintubation

## Slide 107: PRACTICE
Do Exercise 24.3 – Extubation
Performance Evaluation