## Slide 1: RSPT 2335
MODULE A
AIRWAY MANAGEMENT
Part 4
Advanced Airways

## Slide 2: Parts of Module A AIRWAY MANAGEMENT
Part 1 – Pharyngeal, Laryngeal & Esophageal Airways
Part 2 – Tracheal Airways
Part 3 – Airway Clearance
Part 4 - Advanced Airways
Part 5 - Airway Complications & Emergencies

## Slide 3: OBJECTIVES
At the end of this module, the student should be able to…
  describe the different types of endobronchial tubes (EBT).
  explain when an EBT may be indicated.
  given a patient scenario, determine the proper size EBT.
  explain how to determine that the EBT is positioned properly.

## Slide 4: OBJECTIVES
At the end of this module, the student should be able to…
  explain patient transport options with a EBT.
  describe the different unilateral lung procedures that might be necessary
  explain the considerations when ventilating a patient with independent lung ventilation.

## Slide 5: Major Topics
Unilateral Procedures
Endobronchial Tubes
Independent Lung Ventilation

## Slide 6: Unilateral Procedures

## Slide 7: Unilateral Procedures
Bronchoscopy
BAL-Cath sampling
CPT
Side-lying
Left lung suctioning (coude)
Endobronchial intubation
Independent lung ventilation

## Slide 8: Side-lying
Patients normally in upright position
  Maximized lung volumes and capacities
  Decreased VAP risk
Side-lying position with unilateral disease or disorder
  Good lung down
  Increases blood flow to better lung and improves V/Q matching
  Increase in oxygenation and PaO2
  Minimal effect on ventilation and PaCO2

## Slide 9: Left lung suctioning (coude)
What enhances entry into the left lung?
  Coude catheter (L Bronchotrac)
  Supine positioning
  Left side lying
  Head turned to left side
  Tracheostomy tube in place vs. ET tube

## Slide 10: Endobronchial Tubes

## Slide 11: Endobronchial Tubes
Double lumen endobronchial tube (EBT) for independent lung ventilation

## Slide 12: Endobronchial Tubes
About the tube
Indications
Considerations & Precautions

## Slide 13: Endobronchial Tubes
About the tube – types:
  Carlens - Has tracheal hook and is used for entry into left mainstem
  White - Has tracheal hook and is used for entry into right mainstem
  Robertshaw or Mallinckrodt - Designed to enter a mainstem bronchus but does not have a carinal hook

## Slide 14
Endobronchial tube with carinal hook
Carlens
White

## Slide 15
Robertshaw or Mallinckrodt
(no hook)

## Slide 16
Correct positioning of double lumen endobronchial tube.

## Slide 17: WEBSITES
Placement of endobronchial tube by direct laryngoscopy and fiberoptic bronchoscopy (10:57)
www.youtube.com/watch?v=p5NMhVwxlrY

## Slide 18
Often done using bronchoscope or intubation laryngoscope and bronchoscope
About the tube - Placement:

## Slide 19: Endobronchial Tubes
Indications
  Thoracic surgery - pneumonectomy, lobectomy, esophageal resection, aortic aneurysm, cardiac
  Independent lung ventilation
    in presence of unilateral lung problems
    if needed to protect one lung from other
      Disease or blunt trauma
      Bronchopleural fistula
  Bronchospirometry

## Slide 20: Endobronchial Tubes
Considerations & Precautions
  Sizing
  Positioning
  Transport

## Slide 21: Endobronchial Tubes
Considerations & Precautions - Sizing:
  Size: 39 French most common for adults
  Depth: Obtain patient height in cm to determine depth
    1. Height of 179 cm = 29 cm tube
    2. Then add or subtract 1 cm to or from tube length for each 10 cm height difference

## Slide 22: Endobronchial Tubes
Use of bilumen tube in pediatrics
  Children >8 years
    Bronchoport Rusch®
  Neonate and children < 2-3 years
    Marraro Paediatric Endobronchial Bilumen Tube, SIMS - Portex®

## Slide 23: Endobronchial Tubes
Considerations & Precautions – Positioning of tube:
  Insert/verify with bronchoscope
  Auscultate
  Chest wall movement
  Chest x-ray
  Monitor volume return on ventilator
    Example: If inspired volumes do not match expired volumes, complete separation has not been accomplished (check position & cuff pressure)
  Secure properly
  Maintain cuff volumes & pressures

## Slide 24: Endobronchial Tubes
Considerations & Precautions - Transport
  One therapist with one wye adapter and one resuscitation bag
  OR
  Two therapists each with a resuscitation bag

## Slide 25: Transport Do lungs need separate ventilation or can they be combined?

## Slide 26: Endobronchial Tubes
Complications
  inexperience in intubation
  exclusion of the upper lobe bronchus in right bronchial intubation
  dislodgment or obstruction of the tube
  Herniation of the cuff with dislodgement or airway obstruction
  trauma of the trachea and bronchi
  difficult bronchosuctioning

## Slide 27: Independent Lung Ventilation

## Slide 28: Independent Lung Ventilation
Considerations & Precautions – Independent Lung Ventilation
  Synchronous – vents connected by cable
    Lead ventilator controls rate on both
    All other settings can vary
  Asynchronous
    All settings can vary
    If asynchronous (watch EtCO2)
    May increase deadspace ventilation
    May shift mediastinum
    May decrease venous return and cardiac filling/output

## Slide 29: Independent Lung Ventilation
Indications
  Lung pathology with unilateral prevalence
  Bilateral lung pathology complicated by monolateral atelectasis, pneumothorax or fistulae
  Bilateral lung pathology with the patient in obliged to lay on one side
  One lung ventilation during cardiothoracic surgery
  Re-ventilation of the collapsed lung after cardiothoracic surgery. Post-operative phase of cardiothoracic surgery.

## Slide 30: Independent Lung Ventilation
Advantages
  Increase of functional residual capacity and effective ventilation in the more damaged lung
  Reduction of hyperventilation and barotrauma in the less damaged lung
  Use of selective PEEP in the two lungs
  Isolation of secretions of the infected pulmonary areas hence less risk of diffusion of the infection from one lung to the other.
  One lung ventilation during cardiothoracic surgery
  Reventilation of the collapsed lung after cardiothoracic surgery

## Slide 31: Independent Lung Ventilation
Considerations & Precautions – Ventilator settings during synchronized ventilation
  Variable between lungs:
    FiO2
    PEEP
    Mode
    Flows
    Volumes (50% each)
  Same for both lungs:
    Rate

## Slide 32: Independent Lung Ventilation
Considerations & Precautions –
Independent Lung Procedures:
  You must decide which lung & how much
    Aerosol therapy (Bronchodilators, antibiotics, surfactant, mucolytics…)
    Humidification (fluids and heated water bath)
    Suctioning (extra long & smaller 4-6 Fr and separate)
    Graphics
    Mechanics (Cs & Raw)
    EtCO2 Monitoring (monitor Vd)
    Documentation (one form with right and left documented)

## Slide 33: Independent Lung Ventilation
REMOVAL:
  Improvement of chest x-ray
  Reduction of FiO2 < 0.40
  Improvement of compliance