## Slide 1: RSPT 2335
MODULE A
AIRWAY MANAGEMENT
Part 3
Airway Clearance

## Slide 2: Parts of Module A AIRWAY MANAGEMENT
Part 1 – Pharyngeal, Laryngeal & Esophageal Airways
Part 2 – Tracheal Airways
Part 3 – Airway Clearance
Part 4 - Advanced Airways
Part 5 - Airway Complications & Emergencies

## Slide 3: Clinical Practice Guidelines
Endotracheal Suctioning of the Mechanically Ventilated Patients with Artificial Airways (2010)
Bronchoscopy Assisting (2007)
Humidification During Invasive and Non-invasive Mechanical Ventilation (2012)
Nasotracheal Suctioning (2004)

## Slide 4: Assignments
Lab Chapter 36 – Bronchoscopy Assisting
  36.1 – Identification of Components
  36.2 – Preparation of Patient
  36.3 – Preparation of Bronchoscope
  36,4 – Bronchoscopy Procedure
  36.5 – Bronchoscopy Recovery
  36.6 - Bronchoscopy Complications

## Slide 5: OBJECTIVES
At the end of this module, the student should be able to…
  Describe each of the following as it relates to Bronchoscopy according to the AARC’s Clinical Practice Guideline: Fiberoptic Bronchoscopy.
    Process
    Goals
    Indications
    Contraindications
    Hazards
    Complications
  Describe Transtracheal aspiration and explain its purpose.

## Slide 6: Major Topics
Bronchoscopy
Bal-CATH
Rescue Cath
Transtracheal Specimen Collection
The “No Bite V” Suctioning Assist Device

## Slide 7: Bronchoscopy

## Slide 8: Bronchoscope Types
Rigid
Flexible fiberoptic

## Slide 9
Rigid Scope mainly used in O.R.

## Slide 10: Bronchoscopy - Fiberoptic
A diagnostic and/or therapeutic procedure
  A bronchoscope (approximately 3 feet long) is inserted (usually by a physician) into the upper airway and allows direct visualization of the trachea and bronchi.
  RCPs often assist the physician with this procedure.

## Slide 11
Fiberoptic Bronchoscope

## Slide 13
Instillation & tool port

## Slide 14
Fiberoptic Laryngoscopy
Additional tool for intubation

## Slide 15: Bronchoscope Features
Fiberoptic light source for visualization
Suction channel for instilling liquids for cell/secretion removal or coagulation
Lumen for metal alligator forceps, small wire brush or needle to be passed down so tissue specimens can be obtained
Lumen allowing laser for removal of abnormal tissue

## Slide 16
DIAGNOSTIC
(looking for…)
THERAPEUTIC
(treatment of…)
Suspect foreign body
Foreign-body obstruction
Suspect malignancy
Lazar removal of tissue
Pulmonary infections
Removal of secretions from bronchial area (not tracheal)
Hemoptysis
Instillation of meds
Pressure application
Solution to persistent problems
Relief of atelectasis (plug)
Dilation of a stenosis
Purposes for Bronchoscopy

## Slide 17: Responsibilities of the RT During Bronchoscopy
Check the chart – order, lab data, x-ray reports…
Prepare the patient
  Interview (NPO x 8 hours, drug allergies, sedation tolerance…)
  Assess (vital signs, P Ox, breath sounds…)
  Instruct (what to expect)
  Position (semi recumbent)
Obtain vascular access

## Slide 18: Responsibilities of the RT During Bronchoscopy
Prepare and check Bronchoscope
  Light
  Thumb control
  Eyepiece focus
  Patency of suction & biopsy channel
Set-up supplies

## Slide 19: Bronchoscopic Equipment
Bronchoscope(s)
  video/photographic equipment
  cytology brushes, forceps, needles, retrieval baskets
  water soluble lubricant
  sterile gauze
Specimen collection supplies
  PPE
  vacuum equipment
  containers
  fixatives
  syringes
  lavage solutions (saline, mucomyst, epinephrine)
Ventilation supplies
  ventilator adapter
  bite block
Venous access equipment
Medications [atropine, anesthetic, opioid analgesic, benzodiazepines, narcan, topical anesthesia (aerosol & instilled)]
Monitoring devices
  ECG, pulse ox, BP, capnograph
Treatment equipment
Oxygen & equipment
Resuscitation equipment
Intubation equipment
  laryngoscope
  endotracheal tubes
  LMA
Paperwork
Radiology badge (for fluoroscopy)

## Slide 20: Responsibilities of the RT During Bronchoscopy
Prepare the airway
  Pseudoephedrine nasal spray (prevent bleeding)
  Topical anesthetic (Lidocaine)
    by atomizer to nose
    by mouthwash to oral pharynx
    by nebulizer or instilled in bronchoscope to lungs

## Slide 21
Anesthetize the airway

## Slide 22: Responsibilities of the RT During Bronchoscopy
Administer other medications
(per institution policy)
  Oxygen
  Conscious sedation (opioids & benzodiazapines)
  Anticholinergic (atropine or glycopyrrolate)
  Mucomyst (10 – 20%)
  Vaponephrine or Epinephrine (1:10,000)
  Albuterol
Assist with the procedure

## Slide 23: Responsibilities of the RT During Bronchoscopy
Monitor the patient
  Pulse oximeter
  ECG monitor
  BP monitor
Adjust ventilator & O2 as needed
Use bite block or ventilator adapter as needed

## Slide 24
Non-intubated patient needs “Bite Block”
Ventilator Adapter
(Bodai)

## Slide 25: Responsibilities of the RT During Bronchoscopy
Perform post-procedure care of the patient
  Monitor oxygenation & ventilation
  Monitor breath sounds for wheezing or loss of sounds (pneumothorax)
  Keep NPO until anesthetic wears off
  Monitor for airway complications (stridor or laryngospasm)
  Monitor for hemoptysis

## Slide 26: Responsibilities of the RT During Bronchoscopy
Process the specimens
Clean equipment after use (Gluteraldehyde)
Restock bronchoscopy cart
Documentation & billing

## Slide 27: Critical Thinking Question
Would you recommend a rigid or flexible bronchoscopy for Ms. Swanson, a 43-year-old Hispanic woman with a history of hemoptysis. A chest radiograph revealed a mass in her right middle lobe. She is scheduled for a bronchoscopy and possible biopsy.

## Slide 28: Critical Thinking Question
While a bronchoscopy is being performed on a mechanically ventilated patient, you notice the high-pressure alarm is sounding. What are the possible causes and corrective actions?

## Slide 29: Critical Thinking Question
If the physician informs you that the light on the bronchoscope is no longer visible, what would you suggest to correct the problem?

## Slide 30: Critical Thinking Question
A pulmonary fellow is performing her first bronchoscopy and informs you that the entire airway is blurry and suggests instillation of saline to clear the scope. You proceed with the instillation of saline and suction but the field fails to clear. What would you suggest in order to clear the field?

## Slide 31: Critical Thinking Question
A patient with documented hypertension has been schedule for a flexible bronchoscopy. Which of the commonly administered medications during bronchoscopy might cause an adverse reaction? Explain your answer in detail.

## Slide 32: Critical Thinking Question
While assisting with a bronchoscopic procedure for a patient on a mechanical ventilator, you notice that the PEEP has been steadily increasing as the physician inserts the bronchoscope through the endotracheal tube into the airways. What may be the cause of this and what should be done?

## Slide 33: Critical Thinking Question
Mr. Levy is in the recovery room following a bronchoscopy. He is seated upright in bed with a 2 L/min nasal cannula in place. His vital signs are stable but oxygen saturations are beginning to fall below 88%. The patient begins complaining of difficulty breathing. Upon auscultation, you can hear wheezing throughout the upper airways on inspiration and exhalation. What would you suggest be done for this patient?

## Slide 34: Critical Thinking Question
A patient is undergoing a bronchoscopy for removal of thick, inspissated secretions. While assisting with the procedure and monitoring the patient, you note that the patient’s oxygen saturation has fallen from 95% to 84%. Though you have increased the oxygen delivery from 3 L/min nasal cannula to 6 L/min nasal cannula, the oxygen saturation has not changed. What would you suggest be done for this patient?

## Slide 35: Bal-CATH

## Slide 37
Mini-BAL

## Slide 38: Bal-CATH
Bal-CATH is a telescoping catheter with a directional tip that is positioned in the distal airway to obtain an alveolar lavage sample
Used to obtain a lower respiratory tract sputum specimen and improves diagnostic yields over tracheal aspirated or expectorated sputum samples
Has been shown to have similar accuracy to bronchoscopy in obtaining alveolar specimens
It is a disposable, single patient use item.

## Slide 39: Bal-CATH
Purpose:
  Facilitates the diagnosis of diffuse lung disease including pneumonia (used for H1N1)
  Helps identify the organism for more targeted treatment
  Gets a deep lung sample without a bronchoscopy
  May be done by the specially trained RT

## Slide 40
Process:
  A catheter in a sheath is inserted into the lungs to the desired depth
  The catheter alone is then advanced, instillation & suction are performed and the specimen obtained
  The catheter is returned to the sheath then removed.

## Slide 41: Advantages over Bronchoscopy
Can be performed by an RT or RN
Smaller catheter
Shorter procedure (1 – 8 minutes)
Smaller lavage volumes (20 – 40mL) & quicker post procedure stabilization & recovery times
Results similar to bronchoscopy
Directionality is not nearly as important as simply getting a quantitative culture (not contaminated by subglottic secretions

## Slide 42: Care Fusion Video Mini-BAL Mini Bal Demo (7:59 min) DVD

## Slide 43: Rescue Cath

## Slide 44: Rescue Cath

## Slide 45: Rescue Cath

## Slide 46: Rescue Cath

## Slide 48: CAM Rescue Cath
Single use open catheter system for suctioning and removing secretions from endotracheal tube lumen
  Catheter must be calibrated to the length and width of the endotracheal tube to avoid airway injury.
    8 Fr. Rescue-cath for 6.5 – 9.5 mm ID ET
    Align markers on Rescue-cath with ET markers
  Be sure to securely hold the endotracheal tube while using the Rescue-cath to prevent dislodgement.

## Slide 49: CAM Rescue Cath
Each “pass” of the Rescue-cath should last 10 seconds or less
When using the Rescue –cath during ET “cleaning”:
  Inflate balloon with up to 3 mL of air
  Be sure balloon is in endotracheal tube
  do not apply suction
When using the Rescue –cath during ET “suctioning” – keep the balloon deflated

## Slide 50: Transtracheal Sampling

## Slide 51: Transtracheal Sampling
This is a rare physician-performed maneuver:
  A catheter can be inserted through the cricothyroid membrane into the trachea for the purpose of aspirating secretions.
  Uncontaminated specimens can be useful in diagnosing Legionnaire’s Disease.
  Typically a 21-gauge plastic catheter/needle assembly is used.
  Once in place, vacuum system is attached.

## Slide 53: The No Bite V

## Slide 54: The “No Bite V” Suctioning Assist Device
http://www.njrmedical.com/ (5:40)
See No Bite V Inservice:

## Slide 55: The “No Bite V” Suctioning Assist Device
Prevents patient biting down during:
  Oral cleaning
  Oral and tracheal (above the cuff) suctioning
  NG insertion
Illuminates the inside of the mouth for oral assessment
Allows for oral tracheal suctioning vs. nasotracheal suctioning

## Slide 56: The “No Bite V” Suctioning Assist Device
Contraindications – Epiglottitis, croup, pediatrics, acute head, facial or neck injury, coagulopathies, laryngospasm, bronchospasm, MI, URTI, tracheal surgery, high gastric surgery
Potential complications –trauma, hemorrhage, tracheitis, edema, hypoxia, dysrhythmias, vital sign change, coughing, gagging, vomiting, laryngospasm, discomfort, pain, nosocomial infection, atelectasis, increased ICP, IVH, pneumothorax

## Slide 57: The “No Bite V” Suctioning Assist Device
Precautions:
  Obtain physician order before use
  Do not use on pediatric patients
  Do not use on patients with moderate to severe oral disease
  Do not use on patients with recent trauma or surgery to upper airway, larynx or trachea
  Do not twist or try to remove if patient is biting
  Do not use like crow-bar on teeth
  Do not place fingers in mouth or beyond suction insertion hole