## Slide 1: RSPT 2335
Mechanical Ventilation
Module C

## Slide 2: MODULE C - MANAGEMENT LESSONS
Management of the ventilated patient with COPD
Management of the ventilated patient with ASTHMA
Management of the ventilated patient with ARDS
Management of the ventilated patient with OTHER CONDITIONS

## Slide 3: RSPT 2335
Mechanical Ventilation
Module C
MANAGEMENT LESSON #1
COPD

## Slide 4: MODULE C - Assignments
READ: (See First Day Handout)
  Clinical Man & Assess of Resp Dis (7th ed.)
    Chapter 12 – Chronic Obstructive Pulmonary Disease , Chronic Bronchitis, and Emphysema
  Pilbeam (5th ed.) - Mechanical Ventilation
Computer simulation
Lab on Dual Ventilator Modes
  PRVC, VC+, Autoflow
  Volume Support

## Slide 5: MODULE C - Assignments
Optional videotape (E-108):
  Professor’s Rounds 2011 – Management of the Patient with COPD
  Professor's Rounds 2008 – Efficacy of New Modes of Mechanical Ventilation
  Many others under TV in E-108

## Slide 6: MODULE C -Objectives
When you complete this module, you should be able to…
  describe the problems associated with emphysema
  describe the non-invasive methods for caring for COPD patients
  describe the invasive methods for caring for COPD patients
  discuss the different methods for improving CO2 removal

## Slide 7: MODULE C -Objectives
When you complete this module, you should be able to…
  explain which patients may need their CO2 in the normal range
  explain which patients may need hyperventilation techniques
  explain which patients may need permissive hypercapnia techniques

## Slide 8: MODULE C - Objectives
When you complete this module, you should be able to…
  Compare and contrast volume vs. pressure control ventilation.
  Describe the most common pressure modes of ventilation.
  Compare the advantages and disadvantages of the most common modes of ventilation.
  Describe the type of patients suitable for the most common modes.

## Slide 9: MODULE C - Objectives
When you complete this module, you should be able to…
  Draw graphics for each mode.
  List the initial settings for the most common modes.
  Describe the most common dual modes of ventilation.
  List the less common dual modes of ventilation.

## Slide 10: MODULE C Major Topics
COPD Summary
Non-invasive Strategies
Invasive Strategies
Dual Modes Ventilation
Scenario & Case Studies

## Slide 11
Emphysema
What we already know…
COPD SUMMARY

## Slide 12
Enlargement of distal air spaces (remodeling)
Distal airway collapse (loss of elastance)
Alveolar gas trapping
Bronchospasm
Loss of pulmonary capillary bed (diffusion effect)
Decrease surface area for gas exchange
Ventilation in excess of perfusion (deadspace)
C.O.P.D. - ANATOMIC CHANGES

## Slide 13
Dyspnea on exertion
Abnormal PFT
  Decreased FVC, FEV1 & flows
  Increased RV, FRC & RV/TLC ratio
Cough & sputum production
Wheezing, crackles, rhonchi
AmLessory muscle use & tripod use
Pursed lip breathing
Barrel chest
  Decreased - breath & heart sounds, tactile & vocal fremitus
  Hyperresonant percussion
C.O.P.D. - SIGNS & SYMPTOMS

## Slide 14
Abnormal ABG
  Chronic ventilatory failure
  Chronic hypoxemia
Abnormal x-ray *
  Flattened diaphragms
  Hyperlucent lung fields
  Long narrow heart
  Flattened ribs
  Increased retrosternal air space
C.O.P.D. - SIGNS & SYMPTOMS

## Slide 16
C.O.P.D. - SIGNS & SYMPTOMS
Chronic hypoxemia
  Cyanosis
  Increased PAP, PVR, CVP
  Digital clubbing
  Polycythemia
Cor Pulmonale
  JVD
  Hepatomegaly
  Pedal edema

## Slide 17: Goal of Therapy in COPD…
…Empty the lungs!

## Slide 18: Let’s Do A Clinical Simulation
Use simulation tips provided by instructor
Look up things you do not know (PARKING LOT)
Repeat simulations on your own in CE-102

## Slide 19: ICS-7 (Self-Evaluation Software)
Chris Williams – 67 year old Emphysema patient – Critical Care

## Slide 20: MODULE C Major Topics
COPD Summary
Non-invasive Strategies
Invasive Strategies
Dual Modes Ventilation
Scenario & Case Studies

## Slide 21: Non-invasive Management Strategies
Long Term Oxygen Therapy (LTOT)
  Low flow (nasal cannula) & high flow (NC or AEM )
Patient positioning (head up, tri-pod)
Aerosol therapy
  Beta 2 agonists, anticholinergics, methylxanthines, inhaled steroids
Bronchial hygiene
  PEP Therapy, Acapella, flutter, vest…
VamLines & antibiotics (as needed)
Pulmonary Rehabilitation
  Exercise, education, nutrition, smoking cessation…
NIPPV

## Slide 22: MODULE C Major Topics
COPD Summary
Non-invasive Strategies
Invasive Strategies
Dual Modes Ventilation
Scenario & Case Studies

## Slide 23: Invasive Management Strategies
Surgery & Implants
Decrease metabolism (CO2 production)
C. Improve perfusion
D. Optimize ventilation

## Slide 24: Invasive Management Strategies
Surgery
  Bullectomy
  Lung transplant
  Lung volume reduction surgery (LVRS)
  Airway stents & one-way-valves
  PneumRx Wires (new)

## Slide 25: Bullectomy
A Bulla (plural bullae) is an air space in the lung measuring more than one centimeter in diameter in the distended state
http://www.youtube.com/watch?v=cj_uYH2sym4
  VATS (Video-Assisted Thoracoscopic Surgery)
  Removal of a bullae

## Slide 26: Lung Transplantation
Candidates should be projected no more than 2-year survival.
Smoking cessation for at least 6 months prior to surgery.
Age limit
  65 years for single lung transplant.
  60 years for bilateral.
FEV1 & DLCO less than 20% predicted.

## Slide 27: Lung volume reduction surgery (LVRS)
Many people who suffer with emphysema have portions of the lung which are more affected than others.
This finding led to the development of a surgical approach to treat emphysema.
LVRS involves removing about 20 to 30 percent of the damaged lung so that the remaining tissue and surrounding muscles are able to work more efficiently, making breathing easier.
By reducing the lung size, the remaining lung and surrounding muscles (intercostals and diaphragm) are able to work more efficiently.
This makes breathing easier and helps patients achieve greater quality of life.
http://umm.edu/programs/thoracic/services/lvr

## Slide 28: Airway stents & one-way-valves
A new class of minimally invasive interventions delivered through a bronchoscope is under development for improving respiratory function for patients with COPD.
Airway stents can be used to stabilize the patency of some airways while one-way valves or biocompatible glue can be used to close off other airways entirely.
Ideally, one would prefer to use stents to reducing air-trapping in lung regions that are otherwise functional, and to use one way valves and glue to close off lung regions that have lost their gas exchange capability.

## Slide 29
Airway stents

## Slide 30: Endobronchial Valves

## Slide 31: PneumRX
The RePneu Coils are made of Nitinol, a biocompatible, shape-memory alloy.
After being straightened for insertion into the lung, they gather up and compress the diseased lung tissue surrounding them as they return to their original shape.
The Coils improve lung function in three ways:
  Coils compress diseased tissue, which provides room for healthier tissue to function.
  Coils re-tension adjacent parenchyma, which enables the lung to more efficiently contract.
  Coils tether open small airways, which reduces air trapping and hyperinflation.

## Slide 32: Invasive Management Strategies
Surgery
Decrease metabolism (CO2 production)
C. Improve perfusion
D. Optimize ventilation

## Slide 33: Circle of Ventilation
Tissue
Decrease Production
Blood
Improve Carrying
Heart
Improve Pumping
Lungs
Improve Removal
Metabolism: temperature, activity, nutrition, drugs, seizures…
Dissolved + HB
Buffering
Poor perfusion leads to CO2 retention at tissues
Increase rate,
Eliminate auto-PEEP,
Spontaneous breathing,
Therapeutics,
Increase tidal volume,
High frequency vent.

## Slide 34: Optimize Metabolism
Appropriate Nutrition
  Malnutrition can cause muscle fatigue, ventilatory insufficiency, ventilatory failure, muscle atrophy and failure to wean.
  Many COPD patients don’t eat right:
    Too tired or SOB to eat or prepare meals.
    Change in appetite due to meds.
    Change in sense of taste and smell due to oxygen therapy.
    Large meals push up diaphragm and cause SOB.

## Slide 35: Optimize Metabolism
Appropriate Nutrition
  COPD patients can have tremendous increase in calorie needs (up to 3000/day) due to increased work of breathing.
  They need to eat/drink more than normal.
  They need to eat/drink the right things.

## Slide 36: Optimize Metabolism
Decrease CO2 production
  At Home control diet:
    Low carbohydrate diet (Pulmo-care).
    High protein & good fat diets are needed.
  When in hospital:
    Control fever.
    Stop shivering.
    Decrease activity (sedation).
    Evaluate use of stimulants (caffeine…).
    Treat seizures.

## Slide 37: Pulmocare
A high-calorie, low-carbohydrate formula designed to help reduce carbon dioxide production, thereby minimizing CO2 retention resulting from chronic obstructive pulmonary disease, cystic fibrosis, or respiratory failure.
Pulmocare is appropriate for ambulatory or ventilator-dependent patients.

## Slide 38: Circle of Ventilation
Tissue
Decrease Production
Blood
Improve Carrying
Heart
Improve Pumping
Lungs
Improve Removal
Metabolism: temp., activity, nutrition, drugs, seizures…
Dissolved + HB
Buffering
Poor perfusion leads to CO2 retention at tissues
Increase rate,
Eliminate auto-PEEP,
Spontaneous breathing,
Therapeutics,
Increase tidal volume,
High frequency vent.

## Slide 39: Invasive Management Strategies:
Surgery
Decrease metabolism (CO2 production)
C. Improve perfusion
D. Optimize ventilation

## Slide 40: Improve Perfusion
Reduce Air-trapping!!!
  Dynamic hyperinflation and auto-PEEP may produce life threatening cardiac compromise
  Poor perfusion leads to CO2 (acid) retention at the tissues
  CO2 must be pumped back to the lungs for removal

## Slide 41: Circle of Ventilation
Tissue
Decrease Production
Blood
Improve Carrying
Heart
Improve Pumping
Lungs
Improve Removal
Metabolism: temp., activity, nutrition, drugs, seizures…
Dissolved + HB
Buffering
Poor perfusion leads to CO2 retention at tissues
Increase rate,
Eliminate auto-PEEP,
Spontaneous breathing,
Therapeutics,
Increase tidal volume,
High frequency vent.

## Slide 42: Invasive Management Strategies:
Surgery
Decrease metabolism (CO2 production)
C. Improve perfusion
D. Optimize ventilation

## Slide 43: Optimize Ventilation
  Provide therapeutics
  Change modes
  Adjust tidal volume
  Reduce physiologic deadspace by eliminating auto-PEEP
  Reduce mechanical deadspace
  Correct for circuit volume loss
  Adjust rate
  Maintain patient ventilator synchrony
  Allow for spontaneous breathing

## Slide 44: Ventilation
Most critical life function!
If possible - fix this first!
PaCO2 is the best measure of patient's ventilatory status
  For COPD patients the PaCO2 is often >50 mmHg
  Avoid alkalosis - shoot for pH 7.30 – 7.35 range
  CAUTION: Hypoventilation may be the cause of hypoxemia and oxygen therapy is usually indicated to maintain PaO2 >/= 60 mmHg.

## Slide 45: Where should the PaCO2 level be?
PERMISSIVE HYPERCAPNEA (High PaCO2 with pH >7.25)
  ARDS
  Asthma
  Severe pneumonia
  Emphysema
  Severe metabolic alkalosis

## Slide 46: Where should the PaCO2 level be?
NORMOCAPNEA (PaCO2 35 - 45 mmHg)
  Most ventilator patients
  Neuromuscular
  Post-op

## Slide 47: Where should the PaCO2 level be?
HYPERVENTILATION (PaCO2 25 - 30 mmHg)
  Closed Head Injury during times of uncontrolled ICP increases.
  Metabolic acidosis
  Persistent Pulmonary Hypertension (PPH or PFC)

## Slide 48: Apply Appropriate Therapeutics
Patient position (30 – 45 degree head up)
Consider bronchodilation (SABA), (LABA) & steroids
Bronchial hygiene (suctioning, PEP, CPT, IPV, Acapella…)
Consider humidification & hydration
Consider size & type of airway
Consider sedation level
Consider changing position of patient (good lung down)

## Slide 49: Use Proper Mode
Assist control volume ventilation
  Unload muscles
  Watch for hyperinflation and high pressures
  Watch for dysynchrony
Assist control pressure ventilation
  Allows volume & flow variability
  Watch volumes closely
Dual Modes
  Within a breath: VAPS, PAug
  Breath to breath - time cycled: PRVC, Auto-flow, VC+, APV, VPC
  Breath to breath - flow cycled: Volume Support, Smart Care (Drager)
PAV (NPB 840) & PPS (Drager)
NAVA
Smart Care (Drager XL)

## Slide 50: Adjust Ventilator Tidal Volume
Normal lungs being ventilated: 5 – 8 ml/kg IBW.
COPD patient being ventilated: 5 - 8 ml/kg IBW with prolonged expiratory times.
Patient with neuromuscular disorders being ventilated: 7 to 10 ml/kg IBW.
Patient with an acute exacerbation of asthma being ventilated: 4 to 8 ml/kg with prolonged expiratory times.
Patient with ARDS being ventilated: 4 to 8 ml/kg IBW.
Table 7-2 p. 120 Pilbeam

## Slide 51: Adjust Ventilator Tidal Volume
It is not desirable to increase the tidal volume beyond the level appropriate for your patient.
  Ventilator-related lung injury may result from excessive volume delivery.
  Maintain the plateau pressure at or below 30 cm H2O at all times.
Atelectasis & shunt may result from smaller volumes
  Consider increasing PEEP
  Consider using sighs (if available)
  Consider varying the tidal volume breath to breath

## Slide 52: Effective Ventilation
Results of shallow breathing
  decreases effective ventilation
  increased PaCO2
  decreases PaO2
Volumes need to be adequate

## Slide 53: Monitor Physiologic Deadspace
Should the volume or the rate be increased?
  Increasing rates when increased volume is needed may not improve PaCO2.
  Rapid shallow breathing is ineffective.
  It may be more desirable for a patient to increase their spontaneous volume rather than their spontaneous rate.
One solution: Augment Vt with Pressure Support.

## Slide 54: Reduce Physiologic Deadspace
Monitoring Effective Ventilation:
  Calculate:
    Physiologic Vd = Anatomic Vd + Alveolar Vd
    Normal Anatomic (Vd-anat):
      2.2 ml/kg IBW
      1ml/lb. IBW
    Alveolar volume = Vt – Vd-anat
      Normally zero.
      Increased significantly in obstructive disease.

## Slide 55
VA
VD
Vt = VA + VD
Effective Spontaneous Ventilation
(60 – 70%)
3.0 – 5.6 ml/kg IBW
1.5 - 3.2 ml/kg IBW
(30 – 40%)
5 – 8 ml/kg IBW

## Slide 56: How can you decrease anatomic deadspace?
Change to a tracheostomy tube

## Slide 57: How can you decrease alveolar deadspace?
Spontaneous breathing instead of PPV
Decrease excessive PEEP
Decrease excessive volumes or PIP
Decrease auto-PEEP
Improve pulmonary blood flow
  All the above
  Fluids
  Drugs

## Slide 58: Measuring Physiologic Deadspace
Monitoring Effective Ventilation:
  Measure at bedside:
    Capnometry: PaCO2 – PetCO2 gradient
    Volumetric CO2: Effective Ventilation
  Not used clinically:
    Bohr Equation:
      Vd/Vt. ratio (normally 30 – 40%)
      (PaCO2 – PECO2)/ PaCO2 (Douglas bag needed)
_

## Slide 59: Calculation of Deadspace
Capnometry
  Gradient = PaCO2 – PetCO2
  Normal 2 – 6 mm Hg
  Gradient widens with increased deadspace
Volumetric CO2
  Effective Ventilation

## Slide 60: Effective Ventilation
Air-trapping in COPD
  increases alveolar deadspace
  decreases effective ventilation
Needs to be decreased as much as possible

## Slide 61: Eliminate Auto-PEEP
Increase the total cycle time (TCT):
  Decrease rate
Increase expiratory time:
  Decrease rate
  Decrease plateau time

## Slide 62: Eliminate Auto-PEEP
Decrease inspiratory time:
  Volume Ventilation:
    Increase flow
    Decrease tidal volume
  Pressure Ventilation
    Decrease inspiratory time
    Increase I:E ratio
    Decrease pressure
    Adjust Rise time & E sens%

## Slide 63: Eliminate Auto-PEEP
Change to SIMV
Add PS to improve effective vent. and slow the spontaneous rate
Bronchodilate & suction
Check circuit resistance & change HME
Sedate

## Slide 64: Alveolar Volume (VA)
Definition:
  Amount of tidal volume participating in gas exchange
Normal Value: 60 – 70% of Vt or VE
Calculation:
  Tidal Volume – Deadspace Volume = Alveolar Volume
  Vt – Vd-PHYS = VA
  (Vt – Vd-PHYS) x f = VA
.
.

## Slide 65: Alveolar Volume (VA)
Interpretation:
  Decreased alveolar ventilation may lead to:
    Increased PaCO2.
    Decreased PaO2.
  Increased alveolar ventilation may lead to:
    Decreased PaCO2.
    Increased PaO2.

## Slide 66: Scenario
A patient breathing at a rate of 12 breaths/min. has a tidal volume of 600 mL and a measured physiological deadspace of 200 mL. This ventilatory pattern produces a PaCO2 of 40 mmHg.
Several hours later, the patient has a breathing rate of 30 b/min., but the same minute ventilation. Arterial blood gases reveal a PaCO2 of 72 mmHg.
Why has the PaCO2 increased even though the minute ventilation has stayed the same?

## Slide 67: Answer
Initially:
  VE = Vt x f
  = 600 x 12
  = 7,200 mL/min
  VA = (Vt – Vd) x f
  = (600 – 200) x 12
  = 400 x 12
  = 4,800 mL/min
  RSBI = 12/.6L = 20
Later:
  Vt = VE / f
  = 7200 / 30
  = 240 mL
  VA = (Vt – Vd) x f
  = (240 – 200) x 30
  = 40 x 30
  = 1,200 mL
  RSBI = 30/.24L = 125
.
.
.
.

## Slide 68: Don’t forget about Mechanical Deadspace
Caused by equipment place between the wye connector and the patient
Rebreathing of CO2 takes place here
  Examples:
    HME- Do not use if HME Vd > 1/3 Vt.
    Closed suction systems
    MDI chambers
    Capnography adapters
    Long ET tubes (cut or change to trach)
    Elbows
    Flex tubing

## Slide 69
Anything placed between the wye connector and the artificial airway is mechanical deadspace and can cause rebreathing of CO2

## Slide 70: Example of Mechanical Vd
Your patient is a 70 kg IBW (150 lb) male on CPAP of 5 cm H2O with measured spontaneous Vt of 280 mL and a rate of 25. How much effective ventilation does this patient really have?
  Anatomical Vd = 1mL/lb or 150 mL
  Alveolar Vd = 0
  HME Deadspace = 75 mL
  Closed suction Deadspace = 10 mL
  Capnography adapter Deadspace = 10 mL
Answer = [280 – (150 + 75 + 10 + 10)] = 35 mL
(Wonder why he’s not weaning?)

## Slide 71: Don’t forget to Compensate For Circuit Compliance
Most newer ventilators either:
  Compensate for lost volume
  Measure volume at the wye connector (pneumotach)
Servo I, Drager XL, NPB 840 all correct for lost volume correctly “IF”…
    …the circuit and humidifier on the ventilator are warmed up before “Pre-use Check” is done
    …proper humidification device is input on start up

## Slide 72: Don’t forget to Compensate For Circuit Compliance
If the ventilator does not compensate for lost volume in circuit (example: Servo 900C, Servo 300A, home ventilators, VIP Bird) then the set volume must be corrected for lost volume in the circuit:
Patient volume = set volume – lost volume

## Slide 73: Process to Compensate For Circuit Compliance
1. Calculate compliance factor:
  The ventilator circuit is omLluded
  A volume is delivered to the circuit (100 – 150 mL)
  The pressure is measured
  The factor is calculated = Volume / Pressure
  Usually 2 – 4 cm H2O for adult circuit
2. Calculate lost volume = (PIP – PEEP) x C.F.
  Tubing compliance factor is the volume lost in circuit with every cm H2O of ventilating pressure
3. Calculate patient volume = Machine delivered volume – lost volume

## Slide 74: Example of lost volume in circuit
20 kg, 7 year old patient
Patient needs delivered volume of 20 x 10 = 200 mL
Machine volume set at 200 mL
Actual volume delivered to lungs only 125 mL
WHY?
---------------------------------------------------------------------------
Tubing compliance factor 3.0 mL/cmH2O
Ventilating pressure 25 cmH2O
  Lost volume in circuit is 25 x 3.0 = 75 mL
  Set (200) – Lost (75) = 125 mL delivered to patient
Correct problem by readjusting set machine volume to 275mL

## Slide 75: Changing Respiratory Rate
Normal spontaneous rate
  10 – 20 b/min.
Normal ventilator back-up rate
  8 – 12 b/min.
Apnea ventilator back-up rate
  minimum acceptable minute ventilation

## Slide 76: Changing Respiratory Rate
Increasing rate should improve PaCO2.
  Vt x f = MV
  If rate is increased & PaCO2 does not decrease:
    Check for proper Vt or PIP
    Look for excessive mechanical deadspace
    Decrease alveolar deadspace

## Slide 77: Changing Respiratory Rate
Precautions:
  Do not allow rate to increase too much
  High A/C rates > 20/min. can lead to air trapping
    Consider change to SIMV if rate high and air-trapping in AC
  Rate alarms guidelines:
    set at levels appropriate for the patient

## Slide 78: Watch Patient Synchrony
Trigger problems
Change from pressure to flow to NAVA triggering (if available).
Adjust flow triggering properly.
Check system for leaks.
Always use Aero Neb, MDI or intermittent flow with nebulizer breathing treatments.
Get rid of air-trapping and Auto-PEEP.

## Slide 79: Watch Patient Synchrony
Add Applied PEEP:
  If there is uncorrectable auto-PEEP and the patient is having difficulty triggering then consider adding applied PEEP.
    Adds PEEP to the circuit.
    Initial setting 50% of auto-PEEP.
    Increase to 80% of auto-PEEP as needed.
    Stop if increase in PIP is observed.
  Applied PEEP may also help empty the lungs by keeping airways from closing prematurely (2 – 3 cm H2O).

## Slide 80: Watch Patient Synchrony
Inspiratory problems:
  Set inspiratory flow to meet or exceed patient demand
  Typical flow pattern is decelerating
  Be sure the rise time is set properly
  Are there early scoops or spikes?
    Be sure the waveform & peak flow match the patient’s needs

## Slide 81: Watch Patient Synchrony
INSPIRATORY TIME:
Adult 0.8 – 1.2 seconds
Child 0.6 – 0.8 seconds
Infant 0.3 – 0.5 seconds
Smaller volumes in adults require shorter times
Don’t flow starve your patient!!!

## Slide 82: Watch Patient Synchrony
Cycle problems:
Spikes at end of breath?
  Ti too long.
  Volume too large.
Set E sens% properly in pressure support
  COPD tend to like higher E Sens% settings.
Watch for scoops and double trigger.
  Vt may be too low.
  End flow may be too low (try sign or square wave).
  E sens% may be too high.

## Slide 83: Allow For Spontaneous Breathing
Decrease sedation
Changing from complete support to a partial support mode (SIMV or Bi-Level) may:
  Normalize blood gases
  Increase patient comfort
  Recondition respiratory muscles
  Decrease air trapping
Use “Dual Mode” pressure ventilation
  (PRVC, Auto-flow, VC+)
Utilize pressure support and ATC where indicated.
  What is the difference between PSV & ATC?

## Slide 84: Pressure Support
LOW LEVEL - PS <10 cm H2O usually used for overcoming system airflow resistance similar to ATC.
MOD. LEVEL - Begin at 60%- 80% of plateau pressure for spontaneous breathing.
  Usually 10 - 15 cm H2O
  Titrate PS to acceptable rate & Vt
HIGH LEVEL - Beginning at 80% - 100% of plateau pressure is for Psmax (usually >15 cm H2O)
  NOTE: Be sure to set rise time & E% sensitivity properly

## Slide 85: Tracheal Gas Insufflation
A continuous flow of 100% oxygen at 6 L/min is delivered through a small catheter placed through the ET tube 1 cm above the carina.
  A method of expiratory flushing of proximal deadspace gas during mechanical ventilation.
  Used as an adjunct during low tidal volume ventilation to clear CO2 (may allow for less severe hypercapnia).
  Most effective when increased CO2 is due to increased deadspace (Vd/Vt ratio and mechanical).

## Slide 86
Tracheal Gas Insufflation (TGI)

## Slide 87: TGI Complications
Increased volume delivery, PIP & MAP. (increased PaO2?)
Potential for barotrauma & cardiovascular compromise.
Potential for bronchial mucosal damage from catheter & gas flow.
Potential for inspissation & retention of secretions with long term use.

## Slide 88: Optimize Ventilation
  Provide therapeutics
  Change modes
  Adjust tidal volume
  Reduce physiologic deadspace by eliminating auto-PEEP
  Reduce mechanical deadspace
  Correct for circuit volume loss
  Adjust rate
  Maintain patient ventilator synchrony
  Allow for spontaneous breathing

## Slide 89: MODES

## Slide 91
New Form of Ventilator Classification

## Slide 93
Previously discussed modes
Volume Assured Pressure Support (Dual)

## Slide 95
AutoMode

## Slide 96: Modes to Discuss
Manual Targeting Scheme
  Set Point
    Assist control volume ventilation (A/C VCV or CMV-VCV)
    Assist control pressure ventilation (A/C PCV or CMV-PCV)
  Dual
    VAPS – Within a Breath
Automatic Targeting Scheme
  PRVC, Auto-flow, VC+, APV, VPC - Breath to breath - time cycled
  Volume Support, Smart Care - Breath to breath - flow cycled
  AutoMode
  Smart Care
Servo Targeting Scheme
  PAV

## Slide 97: Volume Ventilation
Volume Control Choices
  C - Control
  AC - Assist-Control (CMV)
  A - Assist
  IMV – Intermittent Mandatory Ventilation
  SIMV – Synchronized Intermittent Mandatory Ventilation
  MMV – Mandatory Minute Ventilation

## Slide 98: Volume Ventilation
 | Normal | Increase Cs | Decrease Cs | Increase Raw
Pr |  |  |  | 
Flow |  |  |  | 
Vol |  |  |  | 

## Slide 99: Volume Ventilation
 | Normal | Increase Cs | Decrease Cs | Increase Raw
Pr | Variable |  |  | 
Flow | Set |  |  | 
Vol | Set |  |  | 

## Slide 100: Pressure Ventilation
Pressure Control Choices
  Control
  Assist-Control
  Assist
  IMV
  SIMV
  MMV
OTHER Pressure choices:
  IPPB
  Pressure Support
  ATC
  P-max
  Bi-PAP
  Bi-Level
  APRV
  PRVC
  AUTOFLOW
  VC+
  VS
  AUTOMODE
  SMART CARE
  PAV
  PPS
  ASV
  VAPS
  APS

## Slide 101: Pressure Ventilation
 | Normal | Increase Cs | Decrease Cs | Increase Raw
Pr |  |  |  | 
Flow |  |  |  | 
Vol |  |  |  | 

## Slide 102: Pressure Ventilation
 | Normal | Increase Cs | Decrease Cs | Increase Raw
Pr | Set |  |  | 
Flow | Variable |  |  | 
Vol | Variable |  |  | 

## Slide 105: New Modes
Dual Modes
  Within a breath: VAPS
Automatic
Breath to breath - time cycled: PRVC, Auto-flow, VC+, APV, VPC
Breath to breath - flow cycled: Volume Support, Smart Care (Drager)
Servo
PAV (NPB 840)

## Slide 106: Dual Targeting Scheme
“within a breath”

## Slide 107: Dual Targeting Scheme (within a breath)
1. VAPS – Volume Assured Pressure Support
  (T-BIRD, 8400st)
2. PA - Pressure Augmentation (Bear 1000)
DEFINITION: Pressure support breath with volume control back-up if desired tidal volume is not met.

## Slide 108
Dual Targeting - within one breath
Pressure Supported breath
  Patient effort high
  Pressure met
  Volume delivered
  Flow Cycled
B. Switch from pressure support to flow control
  Patient effort low
  Pressure met/exceeded
  Volume not initially delivered
  Volume Cycled

## Slide 109
VAPS – Variations in breathing pattern
Switch to Volume Ventilation
Flow cycle

## Slide 111: Dual Targeting Scheme (within a breath)
Advantages
  Guaranteed tidal volume in pressure support and A/C mode.
  Less work of breathing than volume control.
  Could improved synchrony more than VCV.
Settings
  Minimal Vt.
  High pressure alarm.
  In PS portion - Pressure support level.
  In AC portion - Peak flow, rate & pressure limit.

## Slide 112: Dual Targeting Scheme (within a breath)
Breath type – machine and/or supported
Trigger to inspiration – machine (time) or patient (flow or pressure)
Inspiratory Phase:
    Volume – set minimum target
    Pressure – PS level set & high pressure limit set
    Rate – machine rate set
    Ti & Te – machine breaths
    Flow – Machine (set) & Pressure Support (variable)
    Waveform –Machine (square) or PS (variable)
    I:E – variable
Cycle to exhalation – Machine (volume) and Spon. (flow)

## Slide 113: Dual Targeting Scheme (within a breath)
Pitfalls
  If PS too high – all breaths are PSV breaths with possibly an excessive tidal volume.
  If Peak flow set too high – breaths will convert to volume ventilation too soon and all breaths will be volume cycled.
  If peak flow too low – asynchrony can occur when Ti becomes too long.
  Pressure can become excessive when switch to volume control occurs.

## Slide 114
VAPS – Variations in breathing pattern

## Slide 115: RSPT 2335
Mechanical Ventilation
Module C
MANAGEMENT LESSON #1
COPD

## Slide 116: MODULE C Major Topics
COPD Summary
Non-invasive Strategies
Invasive Strategies
Dual Modes Ventilation
Scenario & Case Studies

## Slide 117
Emphysema
What we already know…
COPD SUMMARY

## Slide 118: Non-invasive Management Strategies:
Long Term Oxygen Therapy (LTOT)
  Low flow (nasal cannula) & high flow (NC or AEM )
Patient positioning (head up, tri-pod)
Aerosol therapy
  Beta 2 agonists, anticholinergics, methylxanthines, inhaled steroids
Bronchial hygiene
  PEP Therapy, Acapella, flutter, vest…
Vaccines & antibiotics (as needed)
Pulmonary Rehabilitation
  exercise, education, nutrition, smoking cessation…
NIPPV

## Slide 119: Invasive Management Strategies:
Surgery
Decrease metabolism (CO2 production)
C. Improve perfusion
D. Optimize ventilation

## Slide 120: Circle of Ventilation
Tissue
Decrease Production
Blood
Improve Carrying
Heart
Improve Pumping
Lungs
Improve Removal
Metabolism: temp., activity, nutrition, drugs, seizures…
Dissolved + HB
Buffering
Poor perfusion leads to CO2 retention at tissues
Increase rate,
Eliminate auto-PEEP,
Spontaneous breathing,
Therapeutics,
Increase tidal volume,
High frequency vent.

## Slide 121: Optimize Ventilation
  Provide therapeutics
  Change modes
  Adjust tidal volume
  Reduce physiologic deadspace by eliminating auto-PEEP
  Reduce mechanical deadspace
  Correct for circuit volume loss
  Adjust rate
  Maintain patient ventilator synchrony
  Allow for spontaneous breathing

## Slide 122: New Modes
Dual Modes
  Within a breath: VAPS
Automatic
Breath to breath - time cycled: PRVC, Auto-flow, VC+, APV, VPC
Breath to breath - flow cycled: Volume Support, Smart Care (Drager)
Servo
PAV (NPB 840)
NAVA

## Slide 123: Dual Targeting Scheme
“within a breath”

## Slide 124
VAPS – Variations in breathing pattern
Switch to Volume Ventilation
Flow cycle

## Slide 125: Automatic Targeting Scheme
“breath to breath”

## Slide 126: Automatic Targeting Scheme (breath to breath)
Pressure limited & Time cycled with
volume guarantee
Pressure limited & Flow Cycled with
volume guarantee

## Slide 127: Automatic Targeting Scheme (breath to breath)
1. Pressure limited & Time cycled with volume targeted
  PRVC – Pressure Regulated Volume Control (Servo i)
  Auto-flow – (Drager)
  VC+ - Volume Control Plus (NPB 840)
  APV – Adaptive Pressure Ventilation (Hamilton Galileo)
  VPC – Variable Pressure Control (Venturi Vent)

## Slide 128
Automatic Targeting Breath to breath
What is seen on start up or with decreasing compliance or increasing resistance.
Pressure increases 1 – 3 cm H2O per breath to target Vt or maximum pressure.

## Slide 129
Automatic Targeting Breath to breath
Effects of improving compliance or improving resistance
Pressure decreases 1 – 3 cm H2O per breath to maintain target Vt.

## Slide 130
Drager – With Auto-flow turned on there is an automatic change to decelerating flow and free breathing

## Slide 131
Assist control
Pressure ventilation with target volume and maximum pressure limit
Machine pressure level change (#3) caused by tidal volume change
Spontaneous efforts are possible during mandatory inspiration
Volume Control Plus or Auto-flow (CMV or IMV)

## Slide 132: Automatic Targeting Scheme (breath to breath)Time-cycled
Advantages
  Targeted tidal volume in pressure ventilation.
  Automatic weaning of pressure level to lowest setting needed to maintain Vt.
Settings
  Minimal Vt & Max. Vt (if available).
  High pressure alarm (machine can increase pressure to 5 cm H2O below this point).
  Frequency, pressure limit & inspiratory time.

## Slide 133: How to set up PRVC, VC+ & Autoflow
  Mode – machine (CMV or SIMV). *
  Trigger to inspiration – machine or patient (flow or pressure).
  Inspiratory Phase:
    Volume – target set with minimal variation.
    Pressure – Maximum set but otherwise varied by machine to maintain Vt or minute ventilation (limit and alarm).
    Rate – minimum set.
    Ti – set.
    Flow – variable.
    Waveform – variable.
    I:E – variable.
  Cycle to exhalation
    Should be time.
    Will be pressure if pressure > high pressure alarm setting.
      “Volume not constant” alarm will activate

## Slide 134: ALARM: “Volume not constant”
What causes it?
  Changes in compliance, resistance, secretions…. Anything requiring a higher pressure to deliver the set volume target.
  Set volume cannot be delivered within the pressure limit that is set by the practitioner
  Pressure limit is usually 3 – 5 cm H2O below the high pressure alarm setting

## Slide 135: ALARM: “Volume not constant”
What can be done?
  Check for tube placement
  Check breath sounds
    Secretions
    Wheeze
    Absent (effusion, pneumothorax)
  Check for increased auto-PEEP
  Check for agitation
  Decrease the VT
  Increase the pressure

## Slide 136: Automatic Targeting Scheme (breath to breath) Time-cycled
Pitfalls
  If patient demand increases (Vt increases) due to disease or agitation the ventilator will decrease support. In this instant the patient actually needs more support. (runaway)
  Reductions in pressure associated with improved compliance may cause oxygenation to decrease as mean airway pressure falls.
  With disconnect some ventilators begin the ramping process over (840 does not).

## Slide 137: Automatic Targeting Scheme (breath to breath)
2. Pressure limited & Flow Cycled with volume targeted
  VS – Volume Support (Servo 300 & NPB 840)
  VPS – Variable Pressure Support (Venturi)
  Smart Care - Drager

## Slide 138
Volume Support
Pressure support with volume target & maximum pressure

## Slide 139: Automatic Targeting Scheme (breath to breath) Flow-cycled
Advantages
  Targeted tidal volume in pressure support
  Automatic weaning of PSV as patient is able to assume more WOB

## Slide 140: Automatic Targeting Scheme (breath to breath) Flow-cycled
Settings
  Minimum tidal volume (may actually set by minute volume/frequency controls on Servo i)
  High pressure alarm (ventilator can increase pressure support to 5 cm H2O below this value)
  Frequency and tidal volume settings need to be based on proper values for this patient.
    Minimum rate
    NOTE: On some vents tidal volume may increase up to 150% of set to maintain minute ventilation in the face of low rate.

## Slide 141
  Breath type – Spontaneous Supported
  Trigger to inspiration – Patient
  Cycle to exhalation
    Should be flow cycled
    Back-up cycle
      Will time cycle at 80% of TCT
      Will pressure cycle if machine reaches 5 cm H2O above high pressure limit
Automatic Targeting Scheme
(breath to breath)

## Slide 142
Inspiratory Phase:
    Volume – minimal variation (can increase if f decreases to maintain VE).
    Pressure – Maximum set but otherwise varied by machine to maintain Vt or minute ventilation.
    Rate – a target rate is set and if patient rate is < target rate, the machine will increase PS level to increase Vt (up to 150%) and maintain VE.
Automatic Targeting Scheme
(breath to breath)

## Slide 143
Inspiratory Phase:
    Ti – set
    Flow – variable
    Waveform – variable
    I:E – variable
Automatic Targeting Scheme
(breath to breath)

## Slide 144: Automatic Targeting Scheme (breath to breath) Flow-cycled
Pitfalls
  Patient’s may chose to do minimal work and remain at set Vt.
  The PSV level required to maintain a tidal volume may result in auto-PEEP if patient becomes tachypneic.
  If patient demand increases (increased Vt) due to agitation or disease, the ventilator decreases support. In this case, the patient actually needs more support. (runaway)
  If sedation reduces patient respiratory rate or auto-PEEP prevents triggering, a tidal volume of up to 150% of the set volume may be delivered. This may lead to volutrauma or barotrauma.

## Slide 145: Automatic Targeting Scheme
“combinations”

## Slide 146: Automatic Targeting Scheme (combinations)
Pressure Limited & Flow Cycled combined with Pressure Limited & Time Cycled with a volume guarantee
  Automode – (Servo 300A)
  Ventilator is pretty much retired.

## Slide 147: Automatic Targeting Scheme Smart Care - Drager
Similar to volume support.
  Adjusts ventilation to maintain patient in “Zone of Respiratory Comfort” (ZORC).
  Ventilation adjustments based on patient rate, tidal volume, PetCO2, disease, IBW.
  “Disease Classifications” include: Neurological, COPD & normal.

## Slide 148: Let’s do SmartCare Lab together.

## Slide 149: MODES

## Slide 151: Servo Targeting Scheme
Proportional Assist Ventilation (PAV+)
  Watch Puritan Bennett DVD (8 minutes)

## Slide 152: PAV+ (NPB 840)
Proportional Assist Ventilation (PAV+)
  Pressure ventilation: patient triggered, pressure limited & flow-cycled breaths (PS).
  Clinician sets % support (5 – 95%).
    Higher % support = less patient WOB.
  Monitors “Equation of Motion” and adjusts ventilation for changes in:
    compliance
    resistance
    patient effort
  Not for use with low or abnormal respiratory drive, extreme air-trapping, and moderate to large leaks.

## Slide 153
NPB 840 Case Study

## Slide 155: ASV – Adaptive Support Ventilation
Based on the Arthur Otis- “Minimum WOB Concept”.
  Switches ventilator from AC-PC to SIMV-PC with PS to PS ventilation.
  Maintains ventilation and oxygenation, and minimizes work based on compliance, Raw and PEEPi measurement.
  RT inputs IBW, VE, %VE control, PEEP, FiO2, Rise time, flow cycle & high alarm.

## Slide 156: Dual Mode Lab Exercise
Performance Evaluation:
  PRVC, VC+, Autoflow
  VS
Practice on your own and at clinic:
  Smart Care
  PAV

## Slide 157: PRACTICE
Lab Exercise: Modes
  NPB 840 (CMV – VC+ - VS)
  Drager XL (AUTOFLOW)
  Servo I (PRVC – VS)
Performance Evaluation:
  PRVC, VC+, Autoflow
  VS

## Slide 158: Instructor - Scenario #4
Acute Exacerbation of Chronic Airway Obstruction.
  Patient IBW is 63kg
  Square wave flow _____L/sec ____L/min.
  Vt _____L
  PIP _____ cm H2O
  Pplat _____ cm H2O
  PEEP ____ cm H2O
  Rate ______ bpm

## Slide 159: Case studies
Read – Pilbeam
  Case study #5 on page 76
  Case study page 137

## Slide 160: ICS - 11
Janice Wyant – 70 year old COPD patient who recently underwent percutaneous biopsy for chest lesion